## Slide 1
Life Cycle Inventory
Part B Stepwise procedure
Olivier Jolliet, PhD

## Slide 2: Building the inventory: stepwise procedure
Find the direct emission and extraction factors of each unit process (UP, e.g Al hydroxide), i.e. the direct elementary flows per unit of this UP (e.g. MJheat waste/kgAl hydroxide).
Identify the amount of each Unit process per FU, i.e the intermediary flow per functional unit (FU) determined when building the product system and the process tree (e.g. in kgAl hydroxide/FU)
Multiply this amount of each UP per FU (e.g. kgAl hydroxide/FU) by the direct emission or extraction factors of this UP (e.g. MJheat waste/kgAl hydroxide) to calculate the elementary flows of each UP per FU (e.g. MJheat waste/FU)
Calculate the aggregated inventory flows of the total system per FU by summing up all corresponding elementary flows per FU of all UPs.
1
2
3
4
Aluminum
liquid
1 kg
Heat waste
MJ/kgAl liquid
Aluminum
hydroxide
2.96 kg/FU
Heat waste Al hydroxide
MJ/FU
Heat waste
…

## Slide 3: 1. Find the emission and extraction factors: Aluminum primary liquid
Aluminum,
primary,
liquid
1 kg
Transport, transoceanic freight ship 3.8 tkm
Disposal, filter dust Al electrolysis 2.00 g
Electricity mix, aluminum industry 15.9 kWh
Heat, light fuel oil 0.089 MJ
Heat, natural gas 0.084 MJ
Aluminum electrolysis plant 1.54·10-10 p
Aluminum oxide 1.93 kg
Anode, aluminum electrolysis 0.448 kg
Cathode, aluminum electrolysis 0.0181 kg
Disposal, redmud from bauxite digestion 1.36 kg
Nitrogen oxides 63.9 mg
Heat, waste 56.0 MJ/kg Al primary liquid
Hydrogen fluoride 539 mg
Benzo(a)pyrene 1.30 mg
Carbon dioxide, fossil 1.50 kg
Carbon monoxide, biogenic 91.7 g
PAH 45.7 mg
Particulates, < 2.5 µm 2.61 g
Sulfur dioxide 8.83 g
But we also need to collect the direct emission or extraction factors from the unit processes in the entire supply chain
These are the direct emission or extraction from the considered process, i.e. the direct elementary flows per unit of this UP

## Slide 4: Design of process tree: Fill in each box with the process amount per FU
Aluminum oxide
1.93 kg
Anode, aluminum electrolysis
0.449 kg
Cathode, aluminum electrolysis
0.0181 kg
Heat,
light fuel oil
14.9 MJ
Transport, transoceanic freight
34.1 tkm
Electricity mix
57.4 MJ
Disposal, redmud from bauxite digestion
1.36 kg
Disposal, filter dust Al electrolysis
2.00 g
Aluminum, primary,liquid
1 kg
Aluminum hydroxide
2.96 kg
Petroleum coke
0.292 kg
Natural gas
3.19 MJ
Bauxite
4.14 kg
kgAl hydroxide
1.93 x 1.53 = 2.96
kgAl liquid
Use intermediary flows to fill each box with the amount of process used per FU

## Slide 5: 1. Find the emission and extraction factors: Aluminum primary liquid
Aluminum,
hydroxide
1 kg
Water (1.05E-5 m3)
Heat, light fuel oil (3.59 MJ)
Transport, transoceanic freight ship (7.11 tkm)
Total Organic Carbon (18 mg)
Sodium, ion (1.28 g)
Electricity, medium voltage (0.14 kWh)
Heat, waste (0.503 MJ/kgAl hydroxide)
Redmud from bauxite digestion (0.47 kg)
Bauxite at mine 1.4 kg
Suspended solids (0.17 g)
These are the direct emission or extraction from the considered process, i.e. the direct elementary flows per unit of this UP

## Slide 6: 1. Find the emission and extraction factors: Aluminum primary liquid
Aluminum,
hydroxide
1 kg
Water (1.05E-5 m3)
Heat, light fuel oil (3.59 MJ)
Transport, transoceanic freight ship (7.11 tkm)
Total Organic Carbon (18 mg)
Sodium, ion (1.28 g)
Electricity, medium voltage (0.14 kWh)
Heat, waste (0.503 MJ/kgAl hydroxide)
Redmud from bauxite digestion (0.47 kg)
Bauxite at mine 1.4 kg
Suspended solids (0.17 g)
These emissions and extractions factors and elementary flows per unit UP can be found in a) databases, b) literature or websites, or via c) direct data collection via questionnaires with companies or by measurements (usually collected together with the intermediary flows)
These are the direct emission or extraction from the considered process, i.e. the direct elementary flows per unit of this UP

## Slide 7: 1. Find the emission and extraction factor: repeat for all UP
Aluminum oxide
Anode, aluminum electrolysis
Cathode, aluminum electrolysis
Heat,
light fuel oil
Transport, transoceanic freight
Electricity mix
Aluminum, primary,liquid
1 kgAl liquid = FU
Aluminum hydroxide
Bauxite
Transport truck
0.503 MJheat waste/kgAl hydroxide
0.029 MJheat waste/MJlight fuel oil
0.103 MJheat waste/t-km
1.38 MJheat waste/t-km
0.049 MJheat waste/MJ
1.40 MJheat waste/kganode
56.0 MJheat waste/kgAl liquid
Aluminum
oxide
1 kg
0.038 MJheat waste/kgAl oxide
Aluminum
hydroxide
1 kg
Elementary flow per unit UP

## Slide 8: 2. Identify the intermediary flows per functional unit (FU) for all UPs
Aluminum oxide
1.93 kg/FU
Anode, aluminum electrolysis
0.449 kg/FU
Cathode, aluminum electrolysis
0.0181 kg/FU
Heat,
light fuel oil
14.9 MJ/FU
Transport, transoceanic freight
34.1 t∙km/FU
Electricity mix
57.4 kg/FU
Aluminum hydroxide
2.96 kg/FU
Bauxite
4.14 kg/FU
Transport truck
1.21 t∙km/FU
0.503 MJheat waste/kgAl hydroxide
0.029 MJheat waste /MJlight fuel oil
0.103 MJheat waste/t-km
1.38 MJheat waste/t-km
0.049 MJheat waste /MJ
1.40 MJheat waste /kganode
56.0 MJheat waste /kgAl liquid
0.038 MJheat waste/kgAl oxide
When building the product system and process tree, we have determined the intermediary flow of each unit process per Functional Unit, i.e. the amount of each unit process per FU
kgAl hydroxide/kgAl liquid
2.96
Intermediary flow per FU
Elementary flow per unit UP
Aluminum, primary,liquid
1 kgAl liquid = FU

## Slide 9: 3. Combine intermediary and elementary flows for each UP
Aluminum oxide
1.93 kg/FU
Anode, aluminum electrolysis
0.449 kg/FU
Cathode, aluminum electrolysis
0.0181 kg/FU
Heat,
light fuel oil
14.9 MJ/FU
Transport, transoceanic freight
34.1 t∙km/FU
Electricity mix
57.4 kg/FU
Aluminum hydroxide
2.96 kg/FU
Bauxite
4.14 kg/FU
Transport truck
1.21 t∙km/FU
0.503 MJheat waste/kgAl hydroxide
14.9 × 0.029 = 0.43 MJheat waste/FU
34.1 × 0.103
= 1.68 MJheat waste/FU
57.4 × 0.049 = 2.82 MJheat waste/FU
0.449 ×1.40
= 0.63 MJheat waste/FU
1 × 56.0 = 56.0 MJheat waste/kgAl liquid
1.93 × 0.038 = 0.07 MJheat waste/FU
kgAl hydroxide/kgAl liquid
2.96 ×
The inventory is calculated by multiplying the intermediary flow per FU of each unit process by the direct emissions and extractions factors or elementary flows per unit of this same UP
Intermediary flow per FU
Elementary flow per unit UP
Aluminum, primary,liquid
1 kgAl liquid = FU
Elementary flow per FU
1.49 MJheat waste/kgAl liquid
1.21 × 1.38
= 3.51 MJheat waste/FU

## Slide 10: 4. Calculate the aggregated inventory flows of the total system per FU
Aluminum oxide
1.93 kg/FU
Anode, aluminum electrolysis
Cathode, aluminum electrolysis
0.0181 kg/FU
Heat,
light fuel oil
14.9 MJ/FU
Transport, transoceanic freight
34.1 t∙km/FU
Electricity mix
57.4 kg/FU
Aluminum hydroxide
2.96 kg/FU
Bauxite
4.14 kg/FU
Transport truck
1.21 t∙km/FU
0.43 MJheat waste/FU
1.68 MJheat waste/FU
2.82 MJheat waste/FU
0.63 MJheat waste/FU
MJheat waste/FU
0.07 MJheat waste/FU
Sum up all direct CORRESPONDING elementary flows per FU of all unit processes:
Aluminum, primary,liquid
1 kgAl liquid = FU
1.49
MJheat waste/FU
3.51 MJheat waste/FU
Aluminum liquid direct 56.00
Aluminum oxide direct 0.07
Aluminum hydroxide direct 1.49
Anode 0.63
Electricity mix 2.82
Heat, light fuel oil 0.43
Transoceanic freight 1.68
Transport truck 3.51
Aggregated inventory flow
Aluminum liquid 66.6
56.0 MJheat waste/kgAl liquid
0.449 kg/FU

## Slide 11: 4. Aggregated inventory: aluminum primary liquid
Heat, waste (0.503 MJ/kgAl hydroxide)
Aluminum,
primary,
liquid
1 kg
Methane, biogenic 51.7 mg
Uranium in ground 58.3 mg
Aluminum in ground, 24% in bauxite, 11% in crude ore 1.16 kg
Occupation, forest, intensive 0.101 m2a
Crude oil in ground 1.18 kg
Natural gas in ground 525 dm3
Brown coal in ground 1.20 kg
Hard coal in ground 2.01 kg
Nitrogen oxides 19.6 g
Carbon monoxide, biogenic 91.8 g
Heat, waste 66.6 MJ/kg Al primary liquid
Carbon dioxide, fossil 9.40 kg
Arsenic 1.88 mg
Arsenic, ion 44.0 mg
Benzo[a]pyrene 2.74 mg
CFC-14 252 mg
Dioxins 1.74 ng
HFC-116 28.2 mg
Hydrogen fluoride 676 mg
PAH 88.7 mg
Particulates, ,2.5m 4.95 g
Sulfur dioxide 38.0 g

## Slide 12: 4. Aggregated inventory: aluminum primary liquid
What are the intermediary and elementary flows?
Heat, waste (0.503 MJ/kgAl hydroxide)
Aluminum,
primary,
liquid
1 kg
Methane, biogenic 51.7 mg
Uranium in ground 58.3 mg
Aluminum in ground, 24% in bauxite, 11% in crude ore 1.16 kg
Occupation, forest, intensive 0.101 m2a
Crude oil in ground 1.18 kg
Natural gas in ground 525 dm3
Brown coal in ground 1.20 kg
Hard coal in ground 2.01 kg
Nitrogen oxides 19.6 g
Carbon monoxide, biogenic 91.8 g
Heat, waste 66.6 MJ/kg Al primary liquid
Carbon dioxide, fossil 9.40 kg
Arsenic 1.88 mg
Arsenic, ion 44.0 mg
Benzo[a]pyrene 2.74 mg
CFC-14 252 mg
Dioxins 1.74 ng
HFC-116 28.2 mg
Hydrogen fluoride 676 mg
PAH 88.7 mg
Particulates, ,2.5m 4.95 g
Sulfur dioxide 38.0 g

## Slide 13: 4. Aggregated inventory: aluminum primary liquid
These are ALL elementary flows since by definition the aggregated inventory is the sum of all elementary flows per FU of all unit processes
Aluminum,
primary,
liquid
1 kg
Methane, biogenic 51.7 mg
Crude oil in ground 1.18 kg
Natural gas in ground 525 dm3
Brown coal in ground 1.20 kg
Nitrogen oxides 19.6 g
Carbon monoxide, biogenic 91.8 g
Heat, waste 66.6 MJ
Carbon dioxide, fossil 9.40 kg
Arsenic 1.88 mg
Arsenic, ion 44.0 mg
Benzo[a]pyrene 2.74 mg
CFC-14 252 mg
Dioxins 1.74 ng
HFC-116 28.2 mg
Hydrogen fluoride 676 mg
PAH 88.7 mg
Particulates, ,2.5m 4.95 g
Sulfur dioxide 38.0 g
Uranium in ground 58.3 mg
Aluminum in ground, 24% in bauxite, 11% in crude ore 1.16 kg
Occupation, forest, intensive 0.101 m2a
Hard coal in ground 2.01 kg

## Slide 14: Aggregated or unit processes in databases
The ecoinvent database provides two types of data”
  the direct elementary flows and intermediary at unit process level (U=UP level), and
  the aggregated elementary flows of a given product, summed up over the entire supply chain from “cradle to gate” (S=system level)
Many other databases only provide aggregated flows
Such aggregated inventory flows for different processes can be directly used to build the inventory of a new product that combines these different processes.

## Slide 15: Summary
The inventory phase of the LCA determines the elementary flows or emissions and extractions per functional unit, accounting for all processes contributing to the project function.
The inventory is calculated by multiplying the intermediary flow per FU of each unit process by the direct emissions and extractions factors or elementary flows per unit of this same UP.
It is important to distinguish unit process level inventory data that encompass both intermediary and direct elementary flows, from system level inventory data that have already aggregated elementary flows over the product system supply chain, from cradle to gate.
Collecting primary inventory data on intermediary and elementary flows is hard work!