## Slide 1
Primary energy and CO2 balance: Part B data check gCO2 per MJ primary energy
Olivier Jolliet, PhD

## Slide 2: H:C ratio and CO2 emissions
Energy content is associated with the number of H - liaisons
Carbon emissions is associated with the number of C atoms
The ratio of CO2emission/MJ energy is associated with the ratio of H to C
4

## Slide 3: Carbon emissions per unit energy consumption
Source: Nakicenovic, N. and John, A. (1991)

## Slide 4: Checking your data: g CO2 per MJ non renewable primary energy
Concrete
Cement
Mortar
Bio-based materials
Metals
Oil-based materials
Glass
Coal
Oil
Hydraulic
Gas
Wood
Fuels without combustion
Nuclear
Road
Ship
Plane
Emissions [g CO2 / MJ non renewable]
Extracted from ecoinvent 2.2 by Jolliet et al., 2016

## Slide 5: Energy and CO2 balance: light bulb example
1
2a
2b
3a
3b
4

## Slide 6: Check data: interpreting the ratio of g CO2 per MJ non-renewable primary energy
4
Problem detection:
If diesel, oil around 10 gCO2/MJ: combustion is not considered
If plastics around 30 gCO2/MJ, end-of-life (EOL) incineration emissions have been neglected or plastic is deposited in landfill.
If renewable negative, EOL not considered, only fixation of non-fossil CO2
Fossil fuels (transport + heat):
Materials
Oil, diesel, petrol, kerosene
Natural gas
Coke
Electricity US
Electricity Europe
Electricity Switzerland
Fossil materials: plastics, etc.
Metals: depends on % electricity and mix
Concrete
Cement
Wood, cardboard, renewable energy
57-70 gCO2/MJ (incl. 10g pre-combustion) 50 gCO2/MJ
74-94 gCO2/MJ
59 gCO2/MJ
47 gCO2/MJ
13 gCO2/MJ
60 gCO2/MJ (30g manufacturing, 30g elimination) Env. 50 gCO2/MJ
192 gCO2/MJ
227 gCO2/MJ
Also about 65 gCO2/MJ non-renewable fixation not considered: only fossil CO2

## Slide 7: Summary
The primary energy balance and inventory of CO2 emissions is calculated by multiplying the amount of each database process of the process tree by the aggregated emission per unit of this process.
Energy content and carbon are related for fossil fuels
The ratio of gCO2/MJnon renewable primary energy can be used to check the consistency of inventory data
Crucial to account for additional releases during use phase (e.g. combustion emissions) and disposal (e.g. incinerator emissions)