## Slide 1
Full Life Cycle inventory: Car case study Part A Matrix-based inventory calculation
Olivier Jolliet, PhD

## Slide 2: Learning Objectives
Elaborate a full inventory for a simple case study
Illustrate the determination of inventory flows based on aggregated results from database
Perform a sensitivity study on a key uncertain use stage parameter

## Slide 3: Car front-end panel
Function:
transport over car lifetime (200,000 km).
Functional Unit:
1 front-end panel of equivalent rigidity for a 200,000 km service.
System boundaries:
Overall life cycle, including raw material extraction, use stage, end of life treatment.
Front-end panel

## Slide 4: Function and functional units
Steel
Raw material (kg): 10
Required gasoline (L): 80
PRODUCTS OR SYSTEM
REFERENCE FLOWS
KEY ENVIRONMENTAL PARAMETERS
SCENARIO 1
Steel
SCENARIO 2
SMC
FUNCTIONAL UNIT
SCENARIO 3
Aluminum
SMC
Raw material (kg): 7
Required gasoline (L): 56
Aluminum
Raw material (kg): 5.9
Required gasoline (L): 30.4
*200,000 km, additional consumption of 0.00004 L / kg-km
1 front-end- panel of equivalent rigidity for 200,000 km
Final weight of the front end-panel (steel 10kg, SMC 7kg, aluminum 3.8 kg) that directly reflects in the gasoline consumption
Resource consumption per kg of each material
The assumption of 200,000 km over car lifetime

## Slide 5: Automobile component: System boundaries
Energy extraction & preparation, raw materials
Infrastructure, inputs, transportation
Manufacturing
Use
Waste Treatment
Recycling
Resources
Emissions to air, water, soil
SYSTEM BOUNDARIES

## Slide 6: Reference Flows and Main Intermediary Flows
Reference Flows and Main Intermediary Flows for a Front-End Panel Transported over 200,000 km
*200,000 km, additional consumption of 0.00004 L / kg-km
Composite
End of Life
Recycled Aluminum
Virgin Aluminum
Final weight
Incineration
Controlled landfilling
Landfilling for inert materials
Materials
7.0
7.0
–
–
3.8
3.8
–
3.8
–
–
–
–
Steel
Unit
kg
10.0
kg
kg
kg
–
–
10.0
Electricity
Oil
Manufacturing
Gasoline
Use
56.0
30.4
30.4
L
80.0
4.7
0.56
15.2
1.8
15.2
1.8
kWh
kg
19.7
2.3

## Slide 7: Aggregated inventory matrix E

## Slide 8: Inventory calculation
E · y = u
What is the highest contribution to the primary energy?
 Calculate the respective contributions to the total
Steel Front end panel
Steel
Electr.
Oil
Gasoline
Steel disp.