## Slide 1
Building of Product System and Process Tree: Part C – Steps and application to aluminum
Olivier Jolliet, PhD

## Slide 2: Learning Objectives
Build the product system and process tree, more specifically
  Design the process tree of the incandescent light bulb system
  Determine amount of each process per functional unit

## Slide 3: Process tree design
Start from reference flows needed to be purchased per functional unit. Draw one box per reference flow.
Follow the upstream and downstream intermediary flows until you reach processes further (likely to be) covered by an LCA database.
Design the process tree.
For each unit process, document in each box, the amount needed per FU.
1
2
3
4

## Slide 4: Elementary and intermediary flows of Tier 1 Aluminum oxide Unit Process
Illumination
800 lumen
During 5000 h
Electricity 300 kWh
Incandescent light bulb 5 p
From functional unit lecture:
Design the process tree for illumination with incandescent light bulb
5 incandescent bulbs/FU
5000h/FU x 60 W
=300 kWh/FU electricity
PRODUCTS OR SYSTEM
REFERENCE FLOWS (what is purchased)
SCENARIO 1
FUNCTIONAL UNIT (service offered)
800 lumen
for a duration of 5000 hours

## Slide 5: Process Tree: illuminating with incandescent bulbs
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Start with reference flows at Tier 1, draw one box per reference flow
1

## Slide 6: Elementary and intermediary flows of an incandescent bulb
1 incandescent bulb at retail
35.7g
20 g glass
15 g aluminum
10g packaging paper
0.38 MJ primary energy
0.7 g tungsten
1 bulb & 10g packaging to landfill
10,000 km transoceanic freight
3,200 km truck
Use the bulb intermediary flows to design the Tier 2 processes
2

## Slide 7: Process Tree: illuminating with incandescent bulbs
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Transportation
Truck 3200 km
Transportation
Oceanic freight 10,000 km
Paper packaging
Aluminum
Glass
Tungsten
Bulbs to
Landfill
Energy
Design the process tree
3

## Slide 8: Process Tree: illuminating with incandescent bulbs
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Transportation
Truck 3200 km
Transportation
Oceanic freight 10,000 km
Paper packaging
Aluminum
Glass
Tungsten
Bulbs to
Landfill
Energy
5 bulbs/FU x 20g Glass/Bulb
= 100g Glass/FU
5 bulbs/FU x 0.38MJ primary Energy/Bulb
= 1.9 Energy/FU MJ primary
For each unit process, document in each box, the amount needed per FU.
4

## Slide 9: Process tree – illuminating with incandescent bulbs
Paper packaging
50g to recycling
Aluminum to landfill 75g
Glass to landfill
100g
Tungsten to landfill
3.5g
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Transportation
Truck 3200 km
kg∙km
Transportation
Oceanic freight 10,000 km
2,285 kg∙km
Paper packaging
50g
Aluminum
75g
Glass
100g
Tungsten
3.5g
Energy
1.9 MJprimary
TOTAL WEIGHT = 100g + 75g + 3.5g + 50g
= 0.229kg
Also calculate the transportation flows per FU in kg∙km (kg transported over a km)

## Slide 10: Process tree – illuminating with incandescent bulbs
Paper packaging
50g to recycling
Aluminum to landfill 75g
Glass to landfill
100g
Tungsten to landfill
3.5g
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Transportation
Truck 3200 km
731 kg∙km
Transportation
Oceanic freight 10,000 km
2,285 kg∙km
Paper packaging
50g
Aluminum
75g
Glass
100g
Tungsten
3.5g
Energy
1.9 MJprimary
TOTAL WEIGHT = 100g + 75g + 3.5g + 50g
= 0.229kg
TRANSPORTATION = 0.229kg x 3200km
= 731 kg∙km

## Slide 11: Summary
The process tree is an efficient way to visualize the product system.
The intermediary flows enable us to determine the amount of each process used per function unit, in the unit required by the LCI database.
This will serve as the basis to then determine the resource extraction and emission elementary flows of the Life Cycle inventory.
What are the ultimate system boundaries and how to define them consistently?