## Slide 1
Life Cycle Inventory
Calculate the aggregated CO2 emission per FU
Olivier Jolliet, PhD
Notes: Faculty Note:
Enter lecture title, and subtitle if present, in the text box above. Enter name and credentials on the second line as shown. The slide background graphic for this introduction slide can be replaced with an alternate image more suited to the topic or department (this step will be handled by our graphics team in the production phase).

## Slide 2: Building the inventory: stepwise procedure
Find the direct emission and extraction factors of each unit process (UP, e.g Al hydroxide), i.e. the direct elementary flows per unit of this UP (e.g. kgCO2/kgAl hydroxide): See next slide
Identify the amount of each Unit process per FU, i.e the intermediary flow per functional unit (FU) determined when building the product system and the process tree (e.g. in kgAl hydroxide/FU): see next slide
Multiply this amount of each UP per FU (e.g. kgAl hydroxide/FU) by the direct emission or extraction factors of this UP (e.g. kgCO2/kgAl hydroxide) to calculate the elementary flows of each UP per FU (e.g. kgCO2/FU)
Calculate the aggregated inventory flows of the total system per FU by summing up all corresponding elementary flows per FU of all UPs.
1
2
3
4
Aluminum
liquid
1 kg
Aluminum
hydroxide
2.96 kg/FU
CO2 emissions Al hydroxide
kgCO2/FU
CO2 emissions
…

## Slide 3: Calculation of the kgCO2 emitted per kgAl liquid
Aluminum oxide
1.93 kg/FU
Anode, aluminum electrolysis
0.449 kg/FU
Cathode, aluminum electrolysis
0.0181 kg/FU
Heat,
light fuel oil
14.9 MJ/FU
Transport, transoceanic freight
34.1 t∙km/FU
Electricity mix
57.4 MJ/FU
Aluminum, primary,liquid
FU=1 kg
Aluminum hydroxide
2.96 kg/FU
Bauxite
4.14 kg/FU
Q2 Combine intermediary flows per FU with direct emissions to 1) Calculate the emissions of kg carbon dioxide per FU for each process and the total aggregated emissions per FU
2) Identify the two processes contributing most to the total ?
3) Compare the total emission per FU with the
aggregated CO2 emission per FU (slide 4)
0 kgCO2/kgAl hydroxide
0.005 kgCO2/kgBauxite
0.010 kgCO2/t-km
0.094 kgCO2/t-km
0.098 kgCO2/MJ
0.935 kgCO2/kganode
1.50 kgCO2/kgAl liquid
0 kgCO2/kgAl oxide
0.901 kgCO2/kganode
0.090 kgCO2/kgoil
Transport truck
1.21 t∙km/FU
3

## Slide 4: Aggregated inventory: aluminum primary liquid
These are ALL elementary flows since by definition the aggregated inventory is the sum of all elementary flows per FU of all unit processes
Aluminum,
primary,
liquid
1 kg
Methane, biogenic 51.7 mg
Crude oil in ground 1.18 kg
Natural gas in ground 525 dm3
Brown coal in ground 1.20 kg
Nitrogen oxides 19.6 g
Carbon monoxide, biogenic 91.8 g
Heat, waste 66.6 MJ
Carbon dioxide, fossil 9.40 kg
Arsenic 1.88 mg
Arsenic, ion 44.0 mg
Benzo[a]pyrene 2.74 mg
CFC-14 252 mg
Dioxins 1.74 ng
HFC-116 28.2 mg
Hydrogen fluoride 676 mg
PAH 88.7 mg
Particulates, ,2.5m 4.95 g
Sulfur dioxide 38.0 g
Uranium in ground 58.3 mg
Aluminum in ground, 24% in bauxite, 11% in crude ore 1.16 kg
Occupation, forest, intensive 0.101 m2a
Hard coal in ground 2.01 kg
4