## Slide 1
Primary energy and CO2 emissions from processes & materials: Part A Primary, final and useful energy
Olivier Jolliet, PhD

## Slide 2: Learning Objectives
Define primary, final and useful energy
Compare aggregated primary energy and CO2 for various materials and processes

## Slide 3: Primary energy definition
Primary energy is defined as the energy contained in the energy carriers at the point of extraction from the environment, including the upstream energy usage for extraction, preparation, and distribution.
The final energy is the energy purchased by the consumer and delivered to him.
The useful energy is the portion of final energy which is actually available after final conversion to the consumer for the respective use.

## Slide 4: Energy: definitions
Efficiency
Extraction and preparation
Primary energy = including extraction and preparation
Final energy = bought
Useful energy = used
Gas
Electricity
MJ prim
1 MJ final
MJ useful
1 MJ final
MJ useful
MJ prim

## Slide 5: Energy: definitions
Efficiency
Extraction and preparation
Final energy = bought
Useful energy = used
Gas
Electricity
1.25 MJ prim
1 MJ final
0.95 MJ useful
1 MJ final
1 MJ useful
1 kWh final = 3.6 MJ final
1 kWh useful
3.4 MJ prim
Primary energy = including extraction and preparation

## Slide 6: Energy: definitions
Efficiency
Extraction and preparation
Final energy = bought
Useful energy = used
Gas
Electricity
1.25 MJ prim
1 MJ final
0.95 MJ useful
1 MJ final
1 MJ useful
1 kWh final = 3.6 MJ final
1 kWh useful
3.4 MJ prim
12.1 MJ prim
Primary energy = including extraction and preparation

## Slide 7: From ores to primary energy: Net calorific values
Ecoinvent documentation
Density, gross and net calorific value of energy carriers