## Slide 1
Primary Energy and CO2 Balance Part A Stepwise procedure
Olivier Jolliet, PhD

## Slide 2: Learning Objectives
Establish the primary energy and CO2 balance of a product system
Check consistency of inventory data using the gCO2/MJ primary energy

## Slide 3: Process tree – illuminating with incandescent bulbs
Paper packaging
50g to recycling
Aluminum to landfill 75g
Glass to landfill
100g
Tungsten to landfill
3.5g
Illumination
800 lumen
During 5000 h
Electricity
300 kWh
5 Incandescent bulbs
Transportation
Truck 3200 km
731 kg∙km
Transportation
Oceanic freight 10,000 km
2,285 kg∙km
Paper packaging
50g
Aluminum
75g
Glass
100g
Tungsten
3.5g
Energy
1.9 MJprimary
TOTAL WEIGHT = 100g + 75g + 3.5g + 50g
= 0.229kg
TRANSPORTATION = 0.229kg x 3200km
= 731 kg∙km
Glass: 5 bulb x 20 g/bulb = 0.1 kg
Glass: 5 bulb x 10g paper/bulb = 0.05 kg

## Slide 4: Energy and CO2 balance: principles
Total primary energy and CO2 balance: Sum up all contributions to determine the primary energy or CO2 emitted per FU
Data check: Check the consistency between fossil CO2 emissions and non renewable primary energy
List of end processes: Establish the list of DB processed together with their amount per FU (e.g. kgAl/FU) as point of departure
Contribution of each process to energy and CO2 balance: Multiply the amount of each DB process per FU by the aggregated inventory of elementary flow per unit of each DB process (e.g. MJ/kgAl x kgAl/FU = MJ/FU due to Al)
1
2
When building the product system and the process tree, we followed the upstream and downstream intermediary flows until reaching processes covered by an LCA database, named here DB processes.
We documented in the process tree the amount of each of these processes per FU.
3
4

## Slide 5: Energy and CO2 balance: light bulb example
1
2a
2b

## Slide 6: Non-renewable primary energy and CO2 Aggregated inventory flows
Materials
Energy Carriers
Transport
Non-renewable primary
Energy (MJ per unit)
CO2
(kg per unit)
gCO2/MJ
ratio
1 kg paper 20 1 56
1 kg glass 11.5 0.63 55
1 kg aluminum 160 9.5 59
1 kWh electricity (USA) 12.1 0.71 59
1,000 km • kg transport 16-32 ton Lorry 2.6 0.15 58
1 t • km transport (not operation) transoceanic freight 0.17 0.0104 61
 |  |  |  |  |  | Non renewable primary energy MJ | CO2, fossil Air kg | Ratio gCO2/MJ
Dataset-ID | Name | Location | Unit | Ecocat | Ecosubcat |  |  | 
7296 | operation, lorry 16-32t, EURO5 | RER | vkm | transport systems | road | 10.47 | 0.70 | 66.9
7305 | transport, lorry 16-32t, EURO5 | RER | tkm | transport systems | road | 2.58 | 0.15 | 58.1
1961 | operation, transoceanic freight ship | OCE | tkm | transport systems | ship | 0.13 | 0.0088 | 67.7
1968 | transport, transoceanic freight ship | OCE | tkm | transport systems | ship | 0.17 | 0.0104 | 61.2
Ecoinvent 2 process – extract for transportation

## Slide 7: Energy and CO2 balance: light bulb example
1
2a
2b
3a
3b
4